Deliverable for Smart Park (EE)
Alexander Chiem
V636R529

Delivering What
 - A working power system (Primary)
 - Casing (Secondary)

Delivering How
Power System – I will independently research a viable power system. I would like to focus on the rechargeable battery side so we could include a solar panel to recharge and/or condition the battery based on the temperature of the battery. As Dr. Ara mentioned, making use of a voltage regulator will most likely be required and I will also take a look on how to incorporate that as well. I would like to have this research done by the end of March so we can move onto testing it in a real world application.

Casing – I will 3D print a casing that will have all the accommodations that our package requires. This will most likely be a tentative design until a power system is chosen and decisions on any other package modifications.

Delivering When
Power System – Researching (Now – End of March)
Power System – Deliberation and Procurement (April 1 – April 19)
Power System – Testing (As soon as items arrive)

Casing – Designing (Now – April 19)
Casing – Testing and Fitment (As soon as all items arrive)

Delivering Reasoning & Execution

Power System
Since this will be battery powered, I accumulated the typical power consumption from last semester:

ASSUMPTIONS: This is a 3.7V system and the current is in hours.
a) At sleep:
aa1) Arduino: 104 uA
aa2) ToF Sensor:
aaa1) Hardware: 3 – 7 uA, Typical: 5 uA
aaa2) Software: 4 – 9 uA, Typical: 6 uA (Uses 2.8v)
aa3) Magnetometer: 3 uA
aa4) Approx. Total: 114 uA (0.114 mA)
b) At usage:
b1) Arduino Components
bb1) Security Chip: 5mA
bb2) Micro Processor: (On page 988 for DETAILS) 3.4 – 5.73 mA
bb3) LoRa Module: (On Page 6 for DETAILS)	bbb1) Receiving: 21 – 25 mA
bbb2) Sending (no boost): 34 – 47 mA
bbb3) Sending (boosting): 106 – 128 mA
b2) Approx. Total Receiving: 36 mA
b3) Approx. Total Sending: 58 mA (No Boost)
b4) Approx. Total Sending : 139 mA (Boosting)
b5) ToF Sensor: 19 mA
b6) Magnetometer: 2.6 mA (At Peak)
c) Scenarios:
c1) Sending:
cc1) No Boost (On for 24 hours): 58 mA x 24 hrs = 1392 mAh
cc2) Boosting (On for 24 hours): 139 mA x 24 hrs = 3336 mAh
c2) Receiving:
cd1) Receiving (On for 24 Hours): 36 mA x 24 hrs = 864 mAh
c3) Sleeping:
ce1) Sleep (for 24 Hours): 114 uA x 24 hrs = 2736 uA (2.7 mA)
c4) Combinations:
cf1) Send/Recieve (On for 24 Hours):
ccc1) No Boost: 1392 mAh + 864 mAh = 2256 mAh
ccc2) Boosting: 3336 mAh + 864 mAh = 4200 mAh
ccc3) No Boost, All Sensors: 2256 + 456 + 62.4 = 2774.4 mAh
ccc4) Boosting, All Sensors: 4200 + 456 + 62.4 = 4718.4 mAh
c5) ToF Sensor (For 24 hours): 19mA x 24 hrs = 456 mAh
c6) Magnetometer (For 24 Hours): 2.6 mA x 24 hrs = 62.4 mAh

So based off of this, the scenarios were created to see if the system was running 100% for 24 hours. If the system was running in a ‘normal’ mode only needs roughly 2774.4 mAh @ 3.7V while in the boosted mode it requires 4718.4 mAh @ 3.7V. Since this would be the worst case scenario (cars constantly driving over the units), we can take a look at a somewhat more realistic ones.

When it is not sending a signal (it could receive a ‘send status update if it’s changed’), the power consumption will be:

Arduino Components (without sending data) + all the sensors =
5mA + 25mA + 5.73mA + 19mA + 2.6mA = 32.33mA (per hour)

If this package was like this for 24 hours, it would consume only 775.92mA.

Since we had a difficult time maintaining signal integrity (50% success rate) I will focus on using boosted values.

Full usage: 4718.4 (1.0) + 775.92 (0.0) = 4718.4 mAh (24 hours of sending status changes)
75% usage: 4718.4 (0.75) + 775.92 (0.25) = 3732.78 mAh (18 hours of sending status changes)
50% usage: 4718.4 (0.5) + 775.92 (0.5) = 2746.96 mAh (12 hours of sending status changes)
25% usage: 4718.4 (0.25) + 775.92 (0.75) = 1761.54 mAh (6 hours of sending status changes)
0% usage: 4718.4 (0.0) + 775.92 (1.0) = 775.92 mAh (0 hours of sending status changes)
If it was 1 hour: 4718.4 (0.04167) + 775.92 (0.9583) = 940.18 mAh (1 hour of status changes)

From this, a more realistic value to keep in mind would be 50% usage since that would entail 12 hours of consistent status changes. This would accommodate for class times and if there was an event that could extend over an hour or so.

These values come with caveats: These are the listed typical values on the respective data sheets. The magnetometer’s values are not exact as the power consumption data is for another manufacture and was expecting to use that one, but end up using another one. My initial attempt in measuring power consumption did not work as intended since I used a USB power meter and we were powering the system that way over the first semester to test the functions that I completely forgot that I could just use a multi-meter to check.

In terms of collecting actual values, using a multi-meter to check the sensors will be straightforward, but I will need to look into the Arduino’s circuit to see where I can do a current check so I can get a relatively accurate value during usage.

With those power values, my thought is a battery capacity that will operate for 2 days, so roughly a capacity of 5500 mAh @ 3.7V (5.5 Ah * 3.7V = 20.35 Wh)

In terms of battery choices, there is 3 types; 2 are rechargeable and 1 non-rechargeable.

Choice 1 is the Lithium ion types that is most common today. The main pluses is the availability and many different capacities and differing package types to fit multiple needs. The drawbacks is the operating temperatures (Charges at 32F to +113F and discharges at -4F to + 140F), the life cycle (typically less than 300 cycles before it cannot hold 80%), and the possibility other unknown circumstances that could cause the battery to become a safety hazard. (Typical Constant Charge Rate 0.2C = 55mA @ 4.2V; Max @ 3A)

Choice 2 is Lithium Thionyl Chloride (LTC). The main drawback is the non-rechargeable characteristic. The main pluses is this is found in the standard battery sizes (A, AA, AAA, C, D, etc.) so if this was a choice the ability to replace them is straight forward. Other pluses are the availability, while it is not as common as Li-On types, this is still easier to find than my last choice. The operating temperature is quite broad as well (-76F – 185F), can be found in our operating voltage of 3.7V, and it is much less of a hazard than Li-On batteries. If it wasn’t for it being non-rechargeable, I believe this would be the best choice.

Choice 3 is Lithium Titanate (LTO). The main drawbacks is the lack of availability and differing capacities to fit multiple applications. It is typically rated for 2.4V, so this would be a bit difficult to make use of. The pluses is the rechargeable and a much higher charge cycle (around 3000 – 7000 cycles), the batteries are stable, and the temperature range is acceptable (-22F to 131F). This could have been a good choice if we could find it in 3.7V (using a voltage regulator would most likely solve this) and was much more readily available. (Typical Charge Current: 0.5A w/ 5.0A Max and Discharge current is 7.5A

If we choose #2, a solar panel would not be needed, but in turn would require a more regular maintenance. With choices 1 and 2, we could use a solar panel to help recharge the batteries, thus would make it more low maintenance.

A solar panel size to fully charge the battery on a typical sunny day would need a panel rated at 0.775A @ 3.7V (2.8675 W) or 0.57A @ 5V, 0.478A @ 6V, 0.239A @ 12V. Based off a panel that captures 30mA @ 5V is a 2” x1” panel, we would require 16 of these panels. It would roughly be an 8” x 8” panel in total to fully charge the battery in a day (if it was fully exposed to a typical sunny day). This would recharge the battery in a day. If we just want to cover the ‘busy’ days (Mon – Thurs) using a 0.360A @ 3.7V would be sufficient (with the same conditions). This would operate it close to depletion and let it recharge over the weekend. This can be dropped further if the battery consumption is lower if few cars are covering the same spot (less status changes) rather than many cars at the same spot (more status changes).

Deliverables Recap

Based on the power consumption values from last semester, I believe the system may use around 2746.96 mAh @ 3.7V for daily operation. Using a Lithium Ion type battery will be the best choice currently due to availability and many capacities to choose from. This does come with safety concerns, but is still a good choice. With that, a battery capacity to last 2 days (about 5500 mAh @ 3.7V). To recharge this in a single fully exposed sunny day, it would need a panel rated at 0.775A @ 3.7V (2.8675W). A size to let it recharge over the weekend would be 0.360A @ 3.7V in the same conditions. There are some issues with the values (different magnetometer numbers and my interpretation of the values), but this should give me a good foundation to reconsider the battery and solar requirements if my conclusion is off base.